## Slide 1
* Overview of Network layer
  data plane
  control plane
* What’s inside a router
* Generalized Forward and SDN
  Match
  Action
  OpenFlow examples of match-plus-action in action
Outline

## Slide 2: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 3: key network-layer functions
network-layer functions:
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 4: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 5
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 6: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 7
* Overview of Network layer
  data plane
  control plane
* What’s inside a router
* Generalized Forward and SDN
  Match
  Action
  OpenFlow examples of match-plus-action in action
Outline

## Slide 8: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 9: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
switch
fabric

## Slide 10: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
switch
fabric

## Slide 11: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
forwarding table

## Slide 12: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 13: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 14: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 15: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 16: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 17: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 18: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 19: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 20: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
*
N

## Slide 21
* Overview of Network layer
  data plane
  control plane
* What’s inside a router
* Generalized Forward and SDN
  Match
  Action
  OpenFlow examples of match-plus-action in action
Outline

## Slide 22
Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions

## Slide 23: OpenFlow
What is OpenFlow?
OpenFlow is the first and most widely adopted southbound API standard for SDN, enabling communication between the controller and network devices for centralized control of packet forwarding.
OpenFlow Key Concepts
Flow Tables: Packet matching and action rules
Flow Entries: Individual forwarding rules
OpenFlow Channel: Secure connection to controller
OpenFlow Messages: Control protocol messages

## Slide 24: OpenFlow
OpenFlow Switch Architecture
OpenFlow Versions Evolution
OpenFlow 1.0: Basic flow tables and actions
OpenFlow 1.3: Multiple tables, group tables, meters
OpenFlow 1.4+: Extensibility, bundles, synchronization

## Slide 25: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 26: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard

## Slide 27: OpenFlow Actions and Instructions
Required Actions
Output: Send packet to specified port
Drop: Discard packet (no action specified)
Controller: Send packet to controller
Optional Actions
Header Modification Actions:
Set VLAN ID/Priority
Strip VLAN header
Modify MAC addresses
Modify IP addresses
Modify TCP/UDP ports
Modify MPLS labels
Push/Pop MPLS/VLAN headers
Advanced Actions:
Group actions (OpenFlow 1.1+)
Meter actions (OpenFlow 1.3+)
Copy TTL inward/outward
Experimenter actions
Quality of Service Actions:
Set queue for rate limiting
Set DSCP/ToS bits
Apply traffic shaping

## Slide 28: OpenFlow Messages
Message Categories
Controller-to-Switch: Control and configuration messages
Asynchronous: Event notifications from switch
Symmetric: Bidirectional messages
Key OpenFlow Messages
Controller-to-Switch Messages:
Features Request/Reply: Capabilities exchange
Configuration: Switch configuration
Flow Mod: Flow table modifications
Group Mod: Group table modifications
Port Mod: Port configuration
Table Mod: Table configuration
Statistics Request/Reply: Information gathering

## Slide 29: OpenFlow Messages
Key OpenFlow Messages
Asynchronous Messages:
Packet-In: Unmatched packets sent to controller
Flow Removed: Flow entry expiration notification
Port Status: Port state change notification
Error: Error condition reporting
Symmetric Messages:
Hello: Connection establishment
Echo Request/Reply: Keepalive mechanism
Vendor/Experimenter: Vendor-specific extensions
Barrier Request/Reply: Message ordering

## Slide 30: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet / byte counters
Link layer
Network layer
Transport layer
Each flow rule keeps statistics on how many packets matched it.
Notes: Now I’ll describe the API that tries to meet these goals.
30

## Slide 31: Flow Tables and Entries
Example Flow Table
Priority | Match | Action | Counters
100 | in_port = 1, eth_dst = 00:01:02:03:04:05 | output:2 | 1,024 packets
90 | in_port = 1, eth_type = 0x0800, ip_dst = 10.0.0.1 | output:3 | 2,048 packets
50 | in_port=1 | controller | 512 packets
0 | * | drop | 128 packets

## Slide 32
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1

## Slide 33
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
22:A7:23:
11:E1:02

## Slide 34: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices

## Slide 35: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2