## Slide 1: SDN Control Plane

## Slide 2
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 3
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 4
data
plane
control
plane
Recall: logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 5
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming” more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane

## Slide 6: Analogy: mainframe to PC evolution*
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
* Slide courtesy: N. McKeown

## Slide 7: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Notes: Note: implicit assumption here: destination based forwarding

## Slide 8
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance

## Slide 9
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 10
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 11
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 12
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 13
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4

## Slide 14
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 15
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight (ODL) controller
ODL Lithium controller
network apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services

## Slide 16
Network
control apps
…
REST API
ONOS
distributed core
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
Intent
statistics
devices
hosts
links
paths
flow rules
topology
ONOS controller
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling