## Slide 1: Chapter 8: Single-Area OSPF
Routing & Switching
Chapter 5
Notes: Cisco Networking Academy program
Routing Protocols
Chapter 8

## Slide 2: Outline
Characteristics of OSPF
Configuring Single-area OSPFv2
Configure Single-area OSPFv3
Notes: Chapter 8

## Slide 3: Open Shortest Path First Evolution of OSPF
Interior Gateway Protocols
1988
1989
updated in 2008
Notes: 8.1.1.1 Evolution of OSPF

## Slide 4: Open Shortest Path First Features of OSPF
Notes: 8.1.1.2 Features of OSPF

## Slide 5: Open Shortest Path First Components of OSPF
Notes: 8.1.1.3 Components of OSPF

## Slide 6: Open Shortest Path First Components of OSPF (cont.)
OSPF Routers Exchange Packets - These packets are used
To discover neighboring routers
To exchange routing information
To maintain accurate information about the network.
Notes: 8.1.1.3 Components of OSPF (cont.)

## Slide 7: Open Shortest Path First Link-State Operation
If a neighbor is present, the OSPF-enabled router attempts to establish a neighbor adjacency with that neighbor
Notes: 8.1.1.4 Link-State Operation

## Slide 8: Open Shortest Path First Link-State Operation (cont.)
LSAs contain the state and cost of each directly connected link.
Routers flood their LSAs to adjacent neighbors.
Adjacent neighbors receiving the LSA immediately flood the LSA to other directly connected neighbors, until all routers in the area have all LSAs.
Notes: 8.1.1.4 Link-State Operation (cont.)

## Slide 9: Open Shortest Path First Link-State Operation
Build the topology table based on the received LSAs.
This database eventually holds all the information about the topology of the network.
Execute the SPF Algorithm.
Notes: 8.1.1.4 Link-State Operation (cont.)

## Slide 10: Open Shortest Path First Link-State Operation (cont.)
From the SPF tree, the best paths are inserted into the routing table.
Notes: 8.1.1.4 Link-State Operation (cont.)

## Slide 11: Open Shortest Path First Single-area and Multiarea OSPF
Notes: 8.1.1.5 Single-Area and Multiarea OSPF

## Slide 12: Open Shortest Path First Single-area and Multiarea OSPF (cont.)
Notes: 8.1.1.5 Single-Area and Multiarea OSPF (cont.)

## Slide 13: OSPF Messages Encapsulating OSPF Messages
Notes: 8.1.2.1 Encapsulating OSPF Messages

## Slide 14: OSPF Messages Types of OSPF Packets
Notes: 8.1.2.2 Types of OSPF Packets

## Slide 15: OSPF Messages Hello Packet
OSPF Type 1 packet = Hello packet:
Discover OSPF neighbors and establish neighbor adjacencies.
Advertise parameters on which two routers must agree to become neighbors.
Elect the Designated Router (DR) and Backup Designated Router (BDR) on multiaccess networks like Ethernet and Frame Relay.
Notes: 8.1.2.3 Hello Packet

## Slide 16: OSPF Messages Hello Packet (cont.)
Notes: 8.1.2.3 Hello Packet (cont.)

## Slide 17: OSPF Messages Hello Packet Intervals
OSPF Hello packets are transmitted:
To 224.0.0.5 in IPv4 and FF02::5 in IPv6 (all OSPF routers)
Every 10 seconds (default on multiaccess and point-to-point networks)
Every 30 seconds (default on non-broadcast multiaccess [NBMA] networks)
Dead interval is the period that the router waits to receive a Hello packet before declaring the neighbor down
Router floods the LSDB with information about down neighbors out all OSPF enabled interfaces
Notes: 8.1.2.4 Hello Packet Intervals (cont.)

## Slide 18: OSPF Messages Link-State Updates
Notes: 8.1.2.5 Link-State Updates

## Slide 19: OSPF Operation OSPF Operational States
When an OSPF router is initially connected to a network, it attempts to:
Create adjacencies with neighbors
Exchange routing information
Calculate the best routes
Reach convergence
OSPF progresses through several states while attempting to reach convergence.
Notes: 8.1.3.1 OSPF Operational States

## Slide 20: OSPF Operation Establish Neighbor Adjacencies
Notes: 8.1.3.2 Establish Neighbor Adjacencies

## Slide 21: OSPF Operation Establish Neighbor Adjacencies (cont.)
DR and BDR election only occurs on multi-access networks such as Ethernet LANs.
Notes: 8.1.3.2 Establish Neighbor Adjacencies (cont.)

## Slide 22: OSPF Operation OSPF DR and BDR
Notes: 8.1.3.3 OSPF DR and BDR

## Slide 23: OSPF Operation Synchronizing OSPF Database
Notes: 8.1.3.4 Synchronizing OSPF Databases

## Slide 24: OSPF Operation Synchronizing OSPF Database (cont.)
Notes: 8.1.3.4 Synchronizing OSPF Databases

## Slide 25: OSPF Router ID OSPF Network Topology
Notes: 8.2.1.2 Router OSPF Configuration Mode

## Slide 26: OSPF Router ID Router IDs
Notes: 8.2.1.3 Router IDs
8.2.1.4 Configuring an OSPF Router ID
8.2.1.5 Modifying a Router ID
8.2.1.6 Using a Loopback Interface as the Router ID

## Slide 27: Configure Single-area OSPFv2 The network Command
Notes: 8.2.2.1 Enabling OSPF on Interfaces
8.2.2.2 Wildcard Mask
8.2.2.3 The network Command

## Slide 28: Configure Single-Area OSPFv2 Passive Interface
By default, OSPF messages are forwarded out all OSPF-enabled interfaces. However, these messages really only need to be sent out interfaces connecting to other OSPF-enabled routers.
Sending out unneeded messages on a LAN affects the network in three ways:
  Inefficient Use of Bandwidth
  Inefficient Use of Resources
  Increased Security Risk
The Passive Interface feature helps limiting the scope of routing updates advertisements.
Notes: 8.2.2.4 Passive Interface

## Slide 29: Configure Single-area OSPFv2 Configuring Passive Interfaces
Use the passive-interface router configuration mode command to prevent the transmission of routing messages through a router interface, but still allow that network to be advertised to other routers.
Notes: 8.2.2.5 Configuring Passive Interfaces

## Slide 30: OSPF Cost OSPF Metric = Cost
Cost = reference bandwidth / interface bandwidth
(default reference bandwidth is 10^8)
Cost = 100,000,000 bps / interface bandwidth in bps
Notes: 8.2.3.1 OSPF Metric = Cost

## Slide 31: OSPF Cost OSPF Accumulates Costs
Cost of an OSPF route is the accumulated value from one router to the destination network.
Notes: 8.2.3.2 OSPF Accumulates Costs

## Slide 32: OSPF Cost Manually Setting the OSPF Cost
Both the bandwidth interface command and the ip ospf cost interface command achieve the same result, which is to provide an accurate value for use by OSPF in determining the best route.
Notes: 8.2.3.6 Manually Setting the OSPF Cost

## Slide 33: Verify OSPF Verify OSPF Neighbors
Verify that the router has formed an adjacency with its neighboring routers.
Notes: 8.2.4.1 Verify OSPF Neighbors

## Slide 34: Verify OSPF Verify OSPF Protocol Settings
Notes: 8.2.4.2 Verify OSPF Protocol Settings

## Slide 35: OSPFv2 vs. OSPFv3 OSPFv3
Notes: 8.3.1.1 OSPFv3

## Slide 36: OSPFv2 vs. OSPFv3 Similarities Between OSPFv2 to OSPFv3
Notes: 8.3.1.2 Similarities Between OSPFv2 to OSPFv3

## Slide 37: OSPFv2 vs. OSPFv3 Differences Between OSPFv2 to OSPFv3
Notes: 8.3.1.3 Differences Between OSPFv2 and OSPFv3

## Slide 38: OSPFv2 vs. OSPFv3 Link-Local Addresses
FF02::5 address is the all OSPF router address
FF02::6 is the DR/BDR multicast address
Notes: 8.3.1.4 Link-Local Addresses

## Slide 39: Configuring OSFPv3 Configuring the OSPFv3 Router ID
Notes: 8.3.2.4 Configuring the OSPFv3 Router ID

## Slide 40: OSPF Configuring OSFPv3 Enabling OSPFv3 on Interfaces
Instead of using the network router configuration mode command to specify matching interface addresses, OSPFv3 is configured directly on the interface.
Notes: 8.3.2.6 Enabling OSPFv3 on Interfaces

## Slide 41: Verify OSPFv3 Verify OSPFv3 Interfaces
Notes: 8.3.3.3 Verify OSPFv3 Interfaces