## Slide 1: IPv6 Addressing

## Slide 2: Need for IPv6
IPv4 is running out of addresses. IPv6 is the successor to IPv4. IPv6 has a much larger 128-bit address space.
The development of IPv6 also included fixes for IPv4 limitations and other enhancements.
With an increasing internet population, a limited IPv4 address space, issues with NAT and the IoT, the time has come to begin the transition to IPv6.
Notes: 12 – IPv6 Addressing
12.1 – IPv4 Issues
12.1.1 – Need for IPv6

## Slide 3: IPv6 Address Representation
Notes: 12-IPv6 Addressing
12.2 IPv4 Address Representation

## Slide 4: IPv6 Addressing Formats
IPv6 addresses are 128 bits in length and written in hexadecimal.
IPv6 addresses are not case-sensitive and can be written in either lowercase or uppercase.
The preferred format for writing an IPv6 address is x:x:x:x:x:x:x:x, with each “x” consisting of four hexadecimal values.
Examples of IPv6 addresses in the preferred format:
          2001:0db8:0000:1111:0000:0000:0000:0200
          2001:0db8:0000:00a3:abcd:0000:0000:1234
Notes: 12 – IPv6 Addressing
12.2 – IPv6 Address Representation
12.2.1 – IPv6 Addressing Formats

## Slide 5: Rule 1 – Omit Leading Zero
The first rule to help reduce the notation of IPv6 addresses is to omit any leading 0s (zeros).
  Examples:
01ab can be represented as 1ab
09f0 can be represented as 9f0
0a00 can be represented as a00
00ab can be represented as ab
Note: This rule only applies to leading 0s, NOT to trailing 0s, otherwise the address would be ambiguous.
Type | Format
Preferred | 2001 : 0db8 : 0000 : 1111 : 0000 : 0000 : 0000 : 0200
No leading zeros | 2001 : db8 : 0 : 1111 : 0 : 0 : 0 : 200
Notes: 12 – IPv6 Addressing
12.2 – IPv6 Address Representation
12.2.2 – Omit Leading Zero

## Slide 6: Rule 2 – Double Colon
A double colon (::) can replace any single, contiguous string of one or more 16-bit hextets consisting of all zeros.
Example:
2001:db8:cafe:1:0:0:0:1 (leading 0s omitted) could be represented as 2001:db8:cafe:1::1
Note: The double colon (::) can only be used once within an address, otherwise there would be more than one possible resulting address.
Type | Format
Preferred | 2001 : 0db8 : 0000 : 1111 : 0000 : 0000 : 0000 : 0200
Compressed | 2001:db8:0:1111::200
Notes: 12 – IPv6 Addressing
12.2 – IPv6 Address Representation
12.2.2 – Rule 2 – Double Colon
12.2.4 – Activity – IPv6 Address Representation

## Slide 7: IPv6 Address Types
Notes: 12-IPv6 Addressing
12.2 IPv4 Address Types

## Slide 8: Unicast, Multicast, Anycast
There are three broad categories of IPv6 addresses:
Unicast – Unicast uniquely identifies an interface on an IPv6-enabled device.
Multicast – Multicast is used to send a single IPv6 packet to multiple destinations.
Anycast – This is any IPv6 unicast address that can be assigned to multiple devices. A packet sent to an anycast address is routed to the nearest device having that address.
Note: Unlike IPv4, IPv6 does not have a broadcast address. However, there is an IPv6 all-nodes multicast address that essentially gives the same result.
Notes: 12 – IPv6 Addressing
12.3 – IPv6 Address Types
12.3.1 – Unicast, Multicast, Anycast

## Slide 9: IPv6 Address Types
Address Type | Description | Topology
Unicast | “One to One” An address destined for a single interface. A packet sent to a unicast address is delivered to the interface identified by that address. | 
Multicast | “One to Many” An address for a set of interfaces (typically belonging to different nodes). A packet sent to a multicast address will be delivered to all interfaces identified by that address. | 
Anycast | “One to Nearest” (Allocated from Unicast) An address for a set of interfaces. In most cases these interfaces belong to different nodes. A packet sent to an anycast address is delivered to the closest interface as determined by the IGP. | 

## Slide 10: IPv6 Prefix Length
Prefix length is represented in slash notation and is used to indicate the network portion of an IPv6 address.
The IPv6 prefix length can range from 0 to 128. The recommended IPv6 prefix length for LANs and most other types of networks is /64.
Notes: 12 – IPv6 Addressing
12.3 – IPv6 Address Types
12.3.2 – IPv6 Prefix Length

## Slide 11: IPv6 Feature Summary
Increased size of address space
Header simplification
Autoconfiguration
  Stateless (RFC 2462) or stateful (DHCPv6)
  Facilitates renumbering
QoS
  Integrated services (int-serv), Differentiated services (diff-serv and RFC2998)
  RFC 3697
IPSec
  As for IPv4
Transition techniques
  Dual stack
  Tunnelling
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 12: IPv6 header
IPv6 header is simpler than IPv4
  IPv4: 14 fields, variable length (20 bytes +)
  IPv6: 8 fields, fixed length (40 bytes)
Header fields eliminated in IPv6
  Header Length
  Identification
  Flag
  Fragmentation Offset
  Checksum
Header fields enhanced in IPv6
  Traffic Class
  Flow Label
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 13: IPv6 vs IPv4 header
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 14: IPv6 vs IPv4 header
The Traffic Class field is an 8-bit field in the IPv6 header.
Similar to the Type of Service (ToS) field in IPv4.
Allows to classify and prioritize packets (e.g., voice, video, file transfer).
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 15: IPv6 Traffic Class
How it works?
The Traffic Class field is divided into two parts (defined by Differentiated Services – DiffServ):
  Differentiated Services Code Point (DSCP, 6 bits): Defines packet priority/quality of service (QoS).
  Explicit Congestion Notification (ECN, 2 bits): Used for congestion control.
So, the Traffic Class = DSCP (6 bits) + ECN (2 bits).
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 16: IPv6 Traffic Class
Using Class of Traffic (examples)
Network devices (routers, switches, firewalls) read this field to decide how to handle packets:
  High priority (e.g., VoIP, video calls) → Low delay, low loss.
  Normal priority (e.g., web browsing).
  Low priority (e.g., file downloads, background updates).
Example values:
101110xx → Expedited Forwarding (for voice).
001010xx → Assured Forwarding (for streaming).
000000xx → Best Effort (default traffic).
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 17: IPv6 Flow Label
Resource Reservation
IPv6 uses the Flow Label field together with the Traffic Class field to identify these flows.
Flow
A flow is defined as a sequence of packets from a source to a destination with the same properties (e.g., same DSCP, same port).
Protocols Used
RSVP (Resource Reservation Protocol): Used to signal and reserve resources along the path.
Notes: Dual Stack = Devices run IPv4 + IPv6 together.
Tunnelling = IPv6 is "hidden" inside IPv4 packets to cross IPv4-only networks.

## Slide 18: IPv6 Flow Label
Resource Reservation
IPv6 uses the Flow Label field together with the Traffic Class field to identify these flows.
IPv6 Field | Purpose in IntServ
Traffic Class | Marks the type/priority of the flow
Flow Label | Identifies a specific flow across the network
IPv6 Fields used by IntServ
Together, these allow routers to recognize flows and provide per-flow QoS guarantees.